## Slide 1
From Supercomputing
to Metacomputing
Peter Kacsuk
MTA SZTAKI
www.lpds.sztaki.hu

## Slide 2: Agenda
Introduction
The supercomputer era
Clusters
Metacomputers/Grid
European projects
Conclusions

## Slide 3: Progress to Metacomputers
Single processor
2100
Super-computer
2100
2100
2100
2100
2100
2100
2100
2100
Cluster
Meta-computer
GFlops
Computers

## Slide 4: Original motivation for supercomputing
Grand challenge problems run weeks and months even on mainframe single processor computers
Several processors must be connected by high-speed specialised internal networks in order to solve grand challenge problems in reasonable time

## Slide 5: Application areas of supercomputing
Weatherforecast
Scientific computations
  Stellar dynamics
  Life sciences
Engineering computation
  Mechanical Design & Analysis (CAD/CAM)

## Slide 6
Application areas of TOP 500

## Slide 8: The supercomputer era
Breakthrough: Transputers (1984)
Main types:
  Vectorprocessors
    Cray, NEC, Hitachi
    too expensive
  Symmetric multiprocessors
    Sequent, Sun, SGI, IBM
    not scalable
  MPP (Massively Parallel Processors)
    Cray T3E, Intel Paragon, SGI Origin-2000

## Slide 9: Architecture of TOP 500 computer
MPP Vectorproc. Symmetric multiproc. Cluster

## Slide 10: First step to metacomputers
Super-computing
LAN technology
Distributed computing
Clusters

## Slide 11: Three main characteristic features of clusters
1. A cluster connects complete computers (like metacomputers)
2. The component computers of a cluster are loosely connected (like metacomputers)
3. A cluster is utilized as a single, unified computing resource: Single System Image (like supercomputers)

## Slide 12: Two basic cluster types
2. Dedicated clusters (supercomputer-like)
  goal: high performance
  method: parallel computing
  ownership: joint
  strong SSI requirement
1. Nondedicated clusters (NOW: network of workstations)
  goal: usage of spare computing cycles
  method: background job distribution
  ownership: individual owners of workstations
  no SSI requirement

## Slide 13: Structure of a typical nondedicated cluster (NOW)
server
Workstation #1
Workstation #2
Workstation #N
10 Mbit/s ethernet LAN
Other shared devices

## Slide 14: Structure of a typical dedicated cluster
server
Workstation #1
Workstation #2 ...
… Workstation #47
48 port, 24 Gbps switch
100Mbit/s fast ethernet

## Slide 15: Original motivation for metacomputing
Grand challenge problems run weeks and months even on supercomputers and clusters
Various supercomputers/clusters must be connected by wide area networks in order to solve grand challenge problems in reasonable time

## Slide 16: Original meaning of metacomputing
Wide area
network
Original goal of metacomputing:
To achieve higher performance than individual supercomputers/clusters can provide
Super
computing
+
Metacomputing
=

## Slide 17: Second step to metacomputers
Super-computing
WAN technology
Distributed computing
Metacomputers

## Slide 18: What is a Metacomputer?
A metacomputer is a collection of
  computers
  that are heterogeneous in every aspects
  geographically distributed
  connected by a wide-area network
  form the image of a single computer
Metacomputing means:
  network based
  distributed supercomputing

## Slide 19: Further motivations for metacomputing
Better usage of computing and other resources accessible via wide area network
Various computers must be connected by wide area networks in order to exploit their spare cycles
Various special devices must be accessed by wide area networks for collaborative work

## Slide 20: Motivations for grid-computing
To form a computational grid similar to the information data access on the web.
Any computers/devices must be connected by wide area networks in order to form a universal source of computing power.
Grid = generalised metacomputing

## Slide 21: Trends that led to the Grid
Grid
Super-computing
Network technology
Web technology

## Slide 22: What is a Grid?
A Grid is a collection of
  computers, storage and other devices
  that are heterogeneous in every aspects
  geographically distributed
  connected by a wide-area network
  form the image of a single computer
Generalised metacomputing means:
  network based
  distributed computing

## Slide 23: Application areas of the Grid
High throughput computing
  Chip design, parametric studies
Virtual laboratory
  Collaborative design
Data intensive applications
  Sky survey, data mining
Geographic Information systems
Teleimmersion
Enterprise architectures

## Slide 24: Comparison of supercomputers, clusters and metacomputers

## Slide 25: Comparison of supercomputer, cluster and metacomputer sw systems

## Slide 26: Components of a Grid/metacomputing system
Programming models
Architecture issues
Middleware concepts
Programming environments
Scheduling and resource management
Communication media and protocols
System problems like security

## Slide 27: Programming models
Message passing
  PVM, MPI, PVMPI, Globus, PLUS
Macro data-flow
  Webflow, Legion
Object oriented model
  Java, CORBA, DCOM, Legion, Globe
Intelligent mobile agents
  applets, servlets

## Slide 28: Process communication between PVM and MPI via PLUS
C+PVM on workstation cluster
PVM daemon
C+MPI on parallel computer
plus_init()
MPI_receive()
plus_exit()
plus_init()
pvm_send()
plus_exit()
network
Frontend
PLUS daemon

## Slide 29: Middleware concepts
Where is middleware?
Goal of the middleware:
  to turn a radically heterogeneous environment into a virtual homogeneous one
Three main concepts:
  Toolkit (mix-and-match) approach
    Globus
  Object-oriented approach
    Legion, Globe
  Commodity Internet-www approach
    Webflow

## Slide 30: The hourglass concept of Globus
Nexus
protocol
Message passing, Shared memory, IP, etc.
MPI, CC++, HPC++, CORBA, etc.
Internet
protocol
TCP, FTP, HTTP, etc.
Ethernet, ATM, FDDI, etc.
GRAM
protocol
Condor,
LSF, NQE, LoadLeveler, etc.
Resource brokers, Resource co-allocators
High level services
Low level tools

## Slide 31: Globus hierarchical resource management architecture
RSL
Application
Brokers
Run DIS with 100K entities
Information service
Co-allocators
Simple ground RSL
GRAM
GRAM
Run SF-express on 80 nodes
Run SF-express on 256 nodes
Ground RSL
80 nodes on Arg SP-2,
256 nodes on CIT Exemplar
Argonne Resource Manager
CIT Resource Manager
Local resource managers

## Slide 32: Legion
Builds higher level system functionality on top of a single unified object model.
  Objects are themselves processes providing the basis for distribution, scheduling, and resource management
Its software IC concept represents a macro-dataflow technique.
A wide area
network OS
OO computing
environment
+
Legion
=

## Slide 33: Commodity three-tier architectures
Distributed
Objects
Web
architecture
CORBA based
metacomputing
systems
Java based
commodity
metacomputing
Unified
three-tier
metacomputer

## Slide 34: Unified three-tier metacomputer
HTTP
HTTP
Internet
HTTP
W2
W1
W4
Web servers
W3
MPI
MPI service
Protocol perf.opt.
Client application
DC2
DC3
DC1
Distributed computing components
Networked computer server
CORBA
MPP
Database
Stubs
IIOP
skeletons
PC
D
NC
CORBA services

## Slide 35: Programming environments
Toolkit based
  Paderborn toolkit:
    PLUS communication environment
    Resource and Service Description (RSD)
Integrated environments
  VisualGrid (metacomputing version of P-GRADE)
Application specific environments
  NetSolve

## Slide 36: NetSolve
choice
Agent
request
Network of workstations
result
MPP parallel computer
workstations
workstations
Agent
A network-enabled solver to allow the use of network resources for numerical computing
Key concepts: clients - servers - agents

## Slide 37
NetSolve
Reply
Choice
Computational Resources
Hardware: Software:
Clusters Routines
MPP Libraries
Workstations Applications
Globus,Condor, MPI,PVM
Client - RPC like
Matlab
Mathematica
C, Fortran
Java, Excel
Java GUI
Request
Agent
Scheduler
Database

## Slide 38: NetSolve Infrastructure
C
Fortran
Matlab
SCIRun
Custom
PSEs and
Applications
Metacomputing
Resources
Globus
Globus
proxy
Condor
Condor
proxy
NetSolve
NetSolve
NetSolve
proxy
Middleware
Resource Discovery
System Management
Resource Scheduling
Fault Tolerance

## Slide 39: GRID application areas
High throughput computing
Virtual laboratory
Data intenzive applications
  data mining, particle physics
Geographical information systems
Tele-immersion
Enterprise systems

## Slide 40
your
workstation
friendly Condor
personal
Condor
Condor
jobs
Grid
PBS
LSF
Condor
Group
Condor
glide-ins
High throughput Computing: Condor

## Slide 41: The current state of the Grid in the USA
NSF National Technology Grid

## Slide 44: The European DataGrid Project
Department



Desktop
CERN – Tier 0
Tier 1
FNAL
RAL
IN2P3
622 Mbps
2.5 Gbps
622 Mbps
155 mbps
155 mbps
Tier2
Lab a
Uni b
Lab c
Uni n

## Slide 45: Summary
Metacomputing is a new technology which integrates:
  Supercomputing
  Wide-area network technology
  WWW technology
The computational Grid will lead to a new infrastructure similar to the electrical grid
This infrastructure will have a tremendous influence on the Information Society

## Slide 46
Thanks for your attention
?
Further information: www.lpds.sztaki.hu