The inverse z transform

As in the case of Laplace transform, one of the major objectives of the z transform is, that for discrete-time signals (or functions, or models) algebraic manipulations can be made in the z domain and then the final time behaviour is determined by inverse z transformation. In general, the inverse z transform of the complex function  yields information only on , and not on . In other words, the z transform carries information only in a discrete fashion, information on the signals only at the sampling instants. With this in mind, the inverse z transform can be performed by using one of the following three methods:

a) The inversion formula

The time sequence  can be determined from  with the inversion formula:

,	(1.160)

that is a contour integration along the path (, where ( is any closed path (for example a circle centred at the origin) in the z-plane that encloses all singularities of .

One way of evaluation of integral from Equation (1.160) is by use of the residue theorem of complex variable theory. Equation (1.160) is equivalent to writing:

(1.161)

For simple poles, the residue of  at the pole  is obtained as:

.	(1.162)

For a multiple-order q pole , the residue of  at the pole  is:

.	(1.163)

Illustrative example

Given the z transform functions:

a)  and b)

find the inverse z transforms by using the inversion formula (residue theorem).

Solution:

a) The given function has two poles:  and . Formula of Equation (1.162) gives:

b) The given function has a second order pole: . Applying formula (1.163) we get:

.

b) The power series method

In this case, the z transform  is expanded into a power series in powers of . In view of Equation (1.159) the coefficient of  is the value of . The method can be easily programmed on a computer.

Illustrative example

Given the z transform function from the previous example a), find the inverse z transform by using the power series method.

Solution:

The given function can be expanded into a power series in powers of  by long division:

Thus

,

which is the same result as was obtained before.

b) The partial-fraction expansion method

The z transform function is expanded by partial fraction expansion into a sum of simple recognisable terms, and the z transform table is used to determine the corresponding . In carrying out the partial fraction expansion, there is a slight difference between the z transform and the Laplace transform procedures. With reference to the z transform table (Table 1.3), we have to note that practically all the transform functions have the term z in the numerator. Therefor, we should expand  analogous to the partial fraction expansion presented in the case of Laplace transform and then multiply z across to obtain the desired form (for simple zeros), that is:

.	(1.164)

Illustrative example

Given the z transform function from the previous example:

,

find the inverse z transform by using the partial fraction expansion method.

Solution:

Expanding  by partial fraction expansion, we have:

Thus

From the z transform table of Table 1.3., the corresponding inverse z transform is found to be:

,

which is the same result as was obtained in both previous examples.

Important theorems (properties) of the z transform

The following basic theorems extend the usefulness of the z transform method. They help one to obtain a better understanding of z transformations. The theorems are presented shortly, without proofing them.

1. Linearity of the z transform

The z transformation is a linear operation; that is, for any functions  and  whose z transform exists and for any constants  and :

.	(1.165)

2. Real translation (z transform of a time-shifted function)

The real translation makes sense only if the time shift is an integer multiple of the sampling period. We will consider the time-shift equalling to , with n integer.

a)Real translation to the right (time delay)

The z transform of a time-delayed discrete-time function  is equal to the z transform of  multiplied by , that is:

(1.166)

The property is also known as shift into the past.

b)Real translation to the left

The z transform of a discrete-time function shifted to the left  is:

.	(1.167)

The property is also known as shift into the future. By shifting to the left, the function values of the original non-shifted function  for i=0,1,...,n-1 vanish, because the z transform is defined only for positive time sequences.

3. Multiplication by t

The z transform of a time-function  multiplied by its variable t and discretized in time with a sampling period , is:

.	(1.168)

4. Multiplication by

The z transform of the dicretized time-function  is:

.	(1.169)

5. Multiplication by

The z transform of the discretized time-function  is:

.	(1.170)

Notice the change of sign of the coefficient a, or the effect of an exponential damping.

6. Convolution sum

The z transform of the convolution sum over n sampling periods of the discrete-time functions  and  is:

.	(1.171)

7. Initial-value theorem

If the z transform of  is  then:

.	(1.172)

8. Final-value theorem

If the z transform of  is , then the area of the impulse  as  is:

.	(1.173)

The pulse transfer function and the z transfer function

The mathematical model of a system represents the relationships that exist between the input signal  and the output signal  of that particular system. If the considered signals are sampled (time-discretized) by an ideal sampler, the mathematical description of signals is that of infinite impulse trains as was established in Equation (1.94).

The sampler operates at the input of the system as a forcing element that generates periodical impulses. If we consider the time response (the solution of mathematical model) for a singular unitary impulse denoted by the weighting function , the sampler at the output of the system will transform it to the impulse train:

.	(1.174)

The impulse train approximation of the input signal is:

.	(1.175)

The approximate impulse train of the output signal results as a convolution sum (the considered system is linear) over the infinite time interval:

.	(1.176)

This means that for a specific time instant  one obtains:

.	(1.177)

As for the convolution integral for continuous-time systems, the value of the output signal at the time instant  is given by the product sum of  and the opposite time-shifted . The time-shift can be realised either in the impulse response (the weighting function) or in the input signal, as given in Equation (1.176) and/or (1.177).