## Slide 1: Introduction to Embedded Systems Design

## Slide 2: Introduction
What is an Embedded System?
  Application-specific computer system
  Built into a larger system
Why add a computer to the larger system?
  Better performance
  More functions and features
  Lower cost
  More dependability
Economics
  Microcontrollers (used for embedded computers) are high-volume, so recurring cost is low
  Nonrecurring cost dominated by software development
Networks
  Often embedded system will use multiple processors communicating across a network to lower parts and assembly costs and improve reliability

## Slide 3: Options for Building Embedded Systems
Implementation | Design Cost | Unit Cost | Upgrades & Bug Fixes | Size | Weight | Power | System Speed
Discrete Logic | low | mid | hard | large | high | ? | very fast
ASIC | high ($500K/ mask set) | very low | hard | tiny - 1 die | very low | low | extremely fast
Programmable logic – FPGA, PLD | low | mid | easy | small | low | medium to high | very fast
Microprocessor + memory + peripherals | low to mid | mid | easy | small to med. | low to moderate | medium | moderate
Microcontroller (int. memory & peripherals) | low | mid to low | easy | small | low | medium | slow to moderate
Embedded PC | low | high | easy | medium | moderate to high | medium to high | fast
Dedicated Hardware
Software Running on Generic Hardware

## Slide 4: Example Embedded System: Bike Computer
Functions
  Speed and distance measurement
Constraints
  Size
  Cost
  Power and Energy
  Weight
Inputs
  Wheel rotation indicator
  Mode key
Output
  Liquid Crystal Display
Low performance MCU
  8-bit, 10 MIPS

## Slide 5: Benefits of Embedded Computer Systems
Greater performance and efficiency
  Software makes it possible to provide sophisticated control
Lower costs
  Less expensive components can be used
  Manufacturing costs reduced
  Operating costs reduced
  Maintenance costs reduced
More features
  Many not possible or practical with other approaches
Better dependability
  Adaptive system which can compensate for failures
  Better diagnostics to improve repair time

## Slide 6: Embedded System Functions
Closed-loop control system
  Monitor a process, adjust an output to maintain desired set point (temperature, speed, direction, etc.)
Sequencing
  Step through different stages based on environment and system
Signal processing
  Remove noise, select desired signal features
Communications and networking
  Exchange information reliably and quickly

## Slide 7: Attributes of Embedded Systems
Interfacing with larger system and environment
  Analog signals for reading sensors
    Typically use a voltage to represent a physical value
  Power electronics for driving motors, solenoids
  Digital interfaces for communicating with other digital devices
    Simple - switches
    Complex - displays

## Slide 8: Example Analog Sensor - Depth Gauge
Sensor detects pressure and generates a proportional output voltage V_sensor
ADC generates a proportional digital integer (code) based on V_sensor and V_ref
Code can convert that integer to a something more useful
  first a float representing the voltage,
  then another float representing pressure,
  finally another float representing depth
Pressure Sensor
Analog to Digital Converter
// Your software
ADC_Code = ADC0->R[0];
V_sensor = ADC_code*V_ref/1023;
Pressure_kPa = 250 * (V_sensor/V_supply+0.04);
Depth_ft = 33 * (Pressure_kPa – Atmos_Press_kPa)/101.3;
V_sensor
ADC_Code
V_ref
V_sensor
ADC_Code
Voltages
V_ref
Ground
ADC Output Codes
111..111
000..000
000..001
111..110
111..101
111..100
Pressure

## Slide 9: Microcontroller vs. Microprocessor
Both have a CPU core to execute instructions
Microcontroller has peripherals for concurrent embedded interfacing and control
  Analog
  Non-logic level signals
  Timing
  Clock generators
  Communications
    point to point
    network
  Reliability and safety

## Slide 10: Microcontroller vs. Microprocessor
Roughly speaking: MCU= CPU + peripherals (e.g. memory, programmable input/output peripherals )
ARM provides ARM IPs like Cores, internal bus, interrupt controllers, etc.
But MCUs are not created equal! MCUs from different vendors really vary due to different design decisions:
  Architecture
  Implementation
  Processing optimization
  Peripherals
  Power management
  Preferred tool chains
  ……

## Slide 11: Attributes of Embedded Systems
Concurrent, reactive behaviors
  Must respond to sequences and combinations of events
  Real-time systems have deadlines on responses
  Typically must perform multiple separate activities concurrently

## Slide 12: MCU Hardware & Software for Concurrency
CPU executes instructions from one or more thread of execution
Specialized hardware peripherals add dedicated concurrent processing
  DMA - transferring data between memory and peripherals
  Watchdog timer
  Analog interfacing
  Timers
  Communications with other devices
  Detecting external signal events
Peripherals use interrupts to notify CPU of events

## Slide 13: Concurrent Hardware & Software Operation
Embedded systems rely on both MCU hardware peripherals and software to get everything done on time
Hardware
Hardware
Software
Software
Software
Time

## Slide 14: Attributes of Embedded Systems
Fault handling
  Many systems must operate independently for long periods of time, requiring system to handle likely faults without crashing
  Often fault-handling code is larger and more complex than the normal-case code
Diagnostics
  Help service personnel determine problem quickly

## Slide 15: Constraints
Cost
  Competitive markets penalize products which don’t deliver adequate value for the cost
Size and weight limits
  Mobile (aviation, automotive) and portable (e.g. handheld) systems
Power and energy limits
  Battery capacity
  Cooling limits
Environment
  Temperatures may range from -40°C to 125°C, or even more

## Slide 16: Impact of Constraints
Microcontrollers used (rather than microprocessors)
  Include peripherals to interface with other devices, respond efficiently
  On-chip RAM, ROM reduce circuit board complexity and cost
Programming language
  Programmed in C rather than Java (smaller and faster code, so less expensive MCU)
  Some performance-critical code may be in assembly language
Operating system
  Typically no OS, but instead simple scheduler (or even just interrupts + main code (foreground/background system)
  If OS is used, likely to be a lean RTOS

## Slide 17: Curriculum Overview
Introductory Course: Building an Embedded System with an MCU
  Microcontroller concepts
  Software design basics
  ARM Cortex M4 architecture and interrupt system
  C as implemented in assembly language
  Peripherals and interfacing
Advanced Course: Performance Analysis and Optimizations
  Creating responsive systems
  Creating fast systems
  Optimizing system power and energy

## Slide 18: Target Board – STM32F4Discovery
32-bit Cortex-M4 Processor Core
STM32F407VG
  DSP and FPU
  168 MHz max clock
  Up to 1MB Flash/192KB RAM
  Wide range of peripherals, including USB on-the-go
STM32F4Discovery Board
  $20 (USD)
  Peripherals: 3-axis accelerometer, LED, microphone and speaker driver
  Quick breadboard connection and easy probing with compatible expansion headers
  Rich examples, libraries and extra expansion boards available from ST and other third parties

## Slide 19: Why Are We…?
Using C instead of Java (or Python, or your other favorite language)?
  C is the de facto standard for embedded systems because of:
    Precise control over what the processor is doing.
    Modest requirements for ROM, RAM, and MIPS, so much cheaper system
    Predictable behavior, no OS (e.g. Garbage Collection) preemption
Learning assembly language?
  The compiler translates C into assembly language. To understand whether the compiler is doing a reasonable job, you need to understand what it has produced.
  Sometimes we may need to improve performance by writing assembly versions of functions.
Required to have a microcontroller board?
  The best way to learn is hands-on.
  You will keep these boards after the semester ends for possible use in other projects (e.g. Senior Design, Advanced Embedded System Design, Mechatronics, etc.)

## Slide 20: References
ARMv7-M Architecture Reference Manual
The Definitive Guide to ARM® Cortex®-M3 and Cortex®-M4 Processors
STM32F4xx Cortex-M4 programming manual
STM32F407xx Datasheet
STM32F4Discovery User Manual
STM32F40xxx Reference Manual
Application Note 230
  This introduces how to set up the development environment with ARM-MDK