## Slide 1: Software Design Basics

## Slide 2: Overview
Concurrency
  How do we make things happen at the right times?
Software Engineering for Embedded Systems
  How do we develop working code quickly?

## Slide 3: Concurrency

## Slide 4: MCU Hardware & Software for Concurrency
CPU executes instructions from one or more thread of execution
Specialized hardware peripherals add dedicated concurrent processing
  DMA - transferring data between memory and peripherals
  Watchdog timer
  Analog interfacing
  Timers
  Communications with other devices
  Detecting external signal events
Peripherals use interrupts to notify CPU of events

## Slide 5: Concurrent Hardware & Software Operation
Embedded systems rely on both MCU hardware peripherals and software to get everything done on time
Hardware
Hardware
Software
Software
Software
Time

## Slide 6: CPU Scheduling
MCU’s Interrupt system provides a basic scheduling approach for CPU
  “Run this subroutine every time this hardware event occurs”
  Is adequate for simple systems
More complex systems need to support multiple concurrent independent threads of execution
  Use task scheduler to share CPU
  Different approaches to task scheduling
How do we make the processor responsive? (How do we make it do the right things at the right times?)
  If we have more software threads than hardware threads, we need to share the processor.

## Slide 7: Definitions
  TRelease(i) = Time at which task (or interrupt) i requests service/is released/is ready to run
  TLatency (i) = Delay between release and start of service for task i
  TResponse(i) = Delay between request for service and completion of service for task i
  TTask(i) = Time needed to perform computations for task i
  TISR(i) = Time needed to perform interrupt service routine i
Other
processing
Scheduler
Response
Time
Task or ISR Code
Time
Latency
Ttask
TRelease

## Slide 8: Scheduling Approaches
Rely on MCU’s hardware interrupt system to run right code
  Event-triggered scheduling with interrupts
  Works well for many simple systems
Use software to schedule CPU’s time
  Static cyclic executive
  Dynamic priority
    Without task-level preemption
    With task-level preemption

## Slide 9: Event-Triggered Scheduling using Interrupts
Basic architecture, useful for simple low-power devices
  Very little code or time overhead
Leverages built-in task dispatching of interrupt system
  Can trigger ISRs with input changes, timer expiration, UART data reception, analog input level crossing comparator threshold
Function types
  Main function configures system and then goes to sleep
    If interrupted, it goes right back to sleep
  Only interrupts are used for normal program operation
Example: bike computer
  Int1: wheel rotation
  Int2: mode key
  Int3: clock
  Output: Liquid Crystal Display

## Slide 10: Bike Computer Functions
ISR 1: Wheel rotation
ISR 2: Mode Key
ISR 3:
Time of Day Timer
Configure timer,
inputs and
outputs
cur_time = 0;
rotations = 0;
tenth_miles = 0;
while (1) {
sleep;
}
Reset
rotations++;
if (rotations> R_PER_MILE/10) {
tenth_miles++;
rotations = 0;
}
speed =
circumference/
(cur_time – prev_time);
compute avg_speed;
prev_time = cur_time;
return from interrupt
mode++;
mode = mode %
NUM_MODES;
return from interrupt;
cur_time ++;
lcd_refresh--;
if (lcd_refresh==0) {
convert tenth_miles
and display
convert speed
and display
if (mode == 0)
convert cur_time
and display
else
convert avg_speed
and display
lcd_refresh =
LCD_REF_PERIOD
}

## Slide 11: A More Complex Application
GPS-based Pothole Alarm and Moving Map
  Sounds alarm when approaching a pothole
  Display’s vehicle position on LCD
  Also logs driver’s position information
  Hardware: GPS, user switches, speaker, LCD, flash memory

## Slide 12: Application Software Tasks
  Dec: Decode GPS sentence to find current vehicle position.
  Check: Check to see if approaching any pothole locations. Takes longer as the number of potholes in database increases.
  Rec: Record position to flash memory. Takes a long time if erasing a block.
  Sw: Read user input switches. Run 10 times per second
  LCD: Update LCD with map. Run 4 times per second
Dec
Check
Rec
Sw
LCD
Time

## Slide 13: How do we schedule these tasks?
Task scheduling: Deciding which task should be running now
Two fundamental questions
  Do we run tasks in the same order every time?
    Yes: Static schedule (cyclic executive, round-robin)
    No: Dynamic, prioritized schedule
  Can one task preempt another, or must it wait for completion?
    Yes: Preemptive
    No: Non-preemptive (cooperative, run-to-completion)
Dec
Check
Rec
Sw
LCD

## Slide 14: Static Schedule (Cyclic Executive)
Pros
  Very simple
Cons
  Always run the same schedule, regardless of changing conditions and relative importance of tasks.
  All tasks run at same rate. Changing rates requires adding extra calls to the function.
  Maximum delay is sum of all task run times. Polling/execution rate is 1/maximum delay.
Dec
Check
Rec
Sw
LCD
while (1){
Dec();
Check();
Rec();
Sw();
LCD();
}
Dec

## Slide 15: Static Schedule Example
What if we receive GPS position right after Rec starts running?
Delays
  Have to wait for Rec, Sw, LCD before we start decoding position with Dec.
  Have to wait for Rec, Sw, LCD, Dec, Check before we know if we are approaching a pothole!
Dec
Check
Rec
Sw
LCD
GPS Data Arrives
Checking complete
Response Time

## Slide 16: Dynamic Scheduling
Allow schedule to be computed on-the-fly
  Based on importance or something else
  Simplifies creating multi-rate systems
Schedule based on importance
  Prioritization means that less important tasks don’t delay more important ones
How often do we decide what to run?
  Coarse grain – After a task finishes. Called Run-to-Completion (RTC) or non-preemptive
  Fine grain – Any time. Called Preemptive, since one task can preempt another.

## Slide 17: Dynamic RTC Schedule
What if we receive GPS position right after Rec starts running?
Delays
  Have to wait for Rec to finish before we start decoding position with Dec.
  Have to wait for Rec, Dec, Check before we know if we are approaching a pothole
GPS Data Arrives
Checking complete
Response Time
Dec
Check
Rec

## Slide 18: Task State and Scheduling Rules
Scheduler chooses among Ready tasks for execution based on priority
Scheduling Rules
  If no task is running, scheduler starts the highest priority ready task
  Once started, a task runs until it completes
  Tasks then enter waiting state until triggered or released again
Ready
Running
Waiting
Task is released (ready to run)
Task completes
Start highest
priority
ready task

## Slide 19: Dynamic Preemptive Schedule
What if we receive GPS position right after Rec starts running?
Delays
  Scheduler switches out Rec so we can start decoding position with Dec immediately
  Have to wait for Dec, Check to complete before we know if we are approaching a pothole
Dec
Check
GPS Data Arrives
Checking complete
Response Time
Rec

## Slide 20: Comparison of Response Times
Pros
  Preemption offers best response time
    Can do more processing (support more potholes, or higher vehicle speed)
    Or can lower processor speed, saving money, power
Cons
  Requires more complicated programming, more memory
  Introduces vulnerability to data race conditions
Static
Dec
Check
Rec
Sw
LCD
Dec
Check
Rec
Dynamic Run-to-Completion
Dec
Check
Dynamic Preemptive

## Slide 21: Common Schedulers
Cyclic executive - non-preemptive and static
Run-to-completion - non-preemptive and dynamic
Preemptive and dynamic

## Slide 22: Round-Robin with Interrupts
Two priority levels
  main code – foreground
  Interrupts – background
Example of a foreground / background system
Main user code runs in foreground
Interrupt routines run in background (high priority)
  Run when triggered
  Handle most urgent work
  Set flags to request processing by main loop
BOOL DeviceARequest, DeviceBRequest, DeviceCRequest;
void interrupt HandleDeviceA(){
/* do A’s urgent work */
...
DeviceARequest = TRUE;
}
void main(void) {
while (TRUE) {
if (DeviceARequest) {
FinishDeviceA();
}
if (DeviceBRequest) {
FinishDeviceB();
}
if (DeviceCRequest) {
FinishDeviceC();
}
}
}

## Slide 23: Run-To-Completion Scheduler
Use a scheduler function to run task functions at the right rates
  Table stores information per task
    Period: How many ticks between each task release
    Release Time: how long until task is ready to run
    ReadyToRun: task is ready to run immediately
  Scheduler runs forever, examining schedule table which indicates tasks which are ready to run (have been “released”)
  A periodic timer interrupt triggers an ISR, which updates the schedule table
    Decrements “time until next release”
    If this time reaches 0, set that task’s Run flag and reload its time with the period
Follows a “run-to-completion” model
  A task’s execution is not interleaved with any other task
  Only ISRs can interrupt a task
  After ISR completes, the previously-running task resumes
Priority is typically static, so can use a table with highest priority tasks first for a fast, simple scheduler implementation.

## Slide 24: Preemptive Scheduler
Task functions need not run to completion, but can be interleaved with each other
  Simplifies writing software
  Improves response time
  Introduces new potential problems
Worst case response time for highest priority task does not depend on other tasks, only ISRs and scheduler
  Lower priority tasks depend only on higher priority tasks

## Slide 25: Task State and Scheduling Rules
Scheduler chooses among Ready tasks for execution based on priority
Scheduling Rules
  A task’s activities may lead it to waiting (blocked)
  A waiting task never gets the CPU. It must be signaled by an ISR or another task.
  Only the scheduler moves tasks between ready and running
Ready
Running
Waiting
What the
task needs
happens
Task needs
something
to happen
This is
highest
priority
ready task
This isn’t
highest
priority
ready task

## Slide 26: What’s an RTOS?
What does Real-Time mean?
  Can calculate and guarantee the maximum response time for each task and interrupt service routine
  This “bounding” of response times allows use in hard-real-time systems (which have deadlines which must be met)
What’s in the RTOS
  Task Scheduler
    Preemptive, prioritized to minimize response times
    Interrupt support
  Core Integrated RTOS services
    Inter-process communication and synchronization (safe data sharing)
    Time management
  Optional Integrated RTOS services
    I/O abstractions?
    memory management?
    file system?
    networking support?
    GUI??

## Slide 27: Comparison of Timing Dependence
Code can be delayed by everything at same level (in oval) or above
Device A ISR
Device B ISR
Device ... ISR
Device Z ISR
Non-preemptive Static
Preemptive Dynamic
Task 1 Code
Task 4 Code
Task 3 Code
Task 2 Code
Task 6 Code
Task 5 Code
Task 6 Code
Non-preemptive Dynamic
Task 5 Code
Task 4 Code
Task 3 Code
Task 2 Code
Task 1 Code
Device A ISR
Device B ISR
Device ... ISR
Device Z ISR
Task 1 Code
Task 3 Code
Task 2 Code
Task 4 Code
Task 6 Code
Task 5 Code
Device A ISR
Device B ISR
Device ... ISR
Device Z ISR
Slowest Task

## Slide 28: Comparison of RAM Requirements
Preemption requires space for each stack*
Need space for all static variables (including globals)
*except for certain special cases
Non-preemptive Static
Preemptive Dynamic
Non-preemptive Dynamic
Task 1 Max Stack
Task 2 Max Stack
Task 3 Max Stack
Task 4 Max Stack
Task 1 Max Stack
Task 2 Max Stack
Task 3 Max Stack
Task 4 Max Stack
Task 1 Statics
Task 2 Statics
Task 3 Statics
Task 4 Statics
Task 1 Statics
Task 2 Statics
Task 3 Statics
Task 4 Statics
Task 1 Max Stack
Task 2 Max Stack
Task 3 Max Stack
Task 4 Max Stack
Task 1 Statics
Task 2 Statics
Task 3 Statics
Task 4 Statics

## Slide 29: Software Engineering FOR Embedded Systems

## Slide 30: Good Enough Software, Soon Enough
How do we make software correct enough without going bankrupt?
  Need to be able to develop (and test) software efficiently
Follow a good plan
  Start with customer requirements
  Design architectures to define the building blocks of the systems (tasks, modules, etc.)
  Add missing requirements
    Fault detection, management and logging
    Real-time issues
    Compliance to a firmware standards manual
    Fail-safes
  Create detailed design
  Implement the code, following a good development process
    Perform frequent design and code reviews
    Perform frequent testing (unit and system testing, preferably automated)
    Use revision control to manage changes
  Perform post-mortems to improve development process

## Slide 31: What happens when the plan meets reality?
We want a robust plan which considers likely risks
  What if the code turns out to be a lot more complex than we expected?
  What if there is a bug in our code (or a library)?
  What if the system doesn’t have enough memory or throughput?
  What if the system is too expensive?
  What if the lead developer quits?
  What if the lead developer is incompetent, lazy, or both (and won’t quit!)?
  What if the rest of the team gets sick?
  What if the customer adds new requirements?
  What if the customer wants the product two months early?
Successful software engineering depends on balancing many factors, many of which are non-technical!

## Slide 32: Risk Reduction
Plan to the work to accommodate risks
Identify likely risks up front
  Historical problem areas
  New implementation technologies
  New product features
  New product line
Severity of risk is combination of likelihood and impact of failure

## Slide 33: Software Lifecycle Concepts
Coding is the most visible part of a software development process but is not the only one
Before we can code, we must know
  What must the code do? Requirements specification
  How will the code be structured? Design specification
    (only at this point can we start writing code)
How will we know if the code works? Test plan
  Best performed when defining requirements
The software will likely be enhanced over time - Extensive downstream modification and maintenance!
  Corrections, adaptations, enhancements & preventive maintenance

## Slide 34: Product Development Lifecycle
With all this code development and modification, it is worth putting extra effort into simplifying code development activities: understanding, maintaining, enhancing, testing
Diagram: Phil Koopman, Carnegie Mellon University
Coding
Coding
Coding
Coding
Coding
Coding

## Slide 35: Requirements
Ganssle’s Reason #5* for why embedded projects fail: Vague Requirements
Types of requirements
  Functional - what the system needs to do
  Nonfunctional - emergent system behaviors such as response time, reliability, energy efficiency, safety, etc.
  Constraints - limit design choices
Representations
  Text – Liable to be incomplete, bloated, ambiguous, even contradictory
  Diagrams (state charts, flow charts, message sequence charts)
    Concise
    Can often be used as design documents
Traceability
  Each requirement should be verifiable with a test
Stability
  Requirements churn leads to inefficiency and often “recency” problem (most recent requirement change is assumed to be most important)
*Jack Ganssle in an internationally-recognized embedded systems engineer, author and speaker. See http://www.ganssle.com/articles/jackstoptenlist.htm for more on this.

## Slide 36: Design Before Coding
Ganssle’s reason #9: Starting coding too soon
Underestimating the complexity of the needed software is a very common risk
Writing code locks you in to specific implementations
  Starting too early may paint you into a corner
Benefits of designing system before coding
  Get early insight into system’s complexity, allowing more accurate effort estimation and scheduling
  Can use design diagrams rather than code to discuss what system should do and how. Ganssle’s reason #7: Bad Science
  Can use design diagrams in documentation to simplify code maintenance and reduce risks of staff turnover
Architectural Design
Detailed Design
Coding
Test the Code

## Slide 37: Design Before Coding
How much of the system do you design before coding?
AD
DD
C
T
AD
DD
C
T
AD
DD
C
T
AD
C
T
DD
AD
DD
C
T
AD
DD
C
T
AD
DD
C
T
AD
DD
C
T
AD
DD
C
T
Prototyping

## Slide 38: Development Models
How do we schedule these pieces?
Consider amount of development risk
  New MCU?
  Exceptional requirements (throughput, power, safety certification, etc.)
  New product?
  New customer?
  Changing requirements?
Choose model based on risk
  Low: Can create detailed plan. Big-up-front design, waterfall
  High: Use iterative or agile development method, spiral. Prototype high-risk parts first

## Slide 39: Waterfall (Idealized)
Plan the work, and then work the plan
BUFD: Big Up-Front Design
Model implies that we and the customers know
  All of the requirements up front
  All of the interactions between components, etc.
  How long it will take to write the software and debug it
Diagram: Jon McCormack, Monash University

## Slide 40: Waterfall (As Implemented)
Reality: We are not omniscient, so there is plenty of backtracking
Diagram: Jon McCormack, Monash University

## Slide 41: Agile Development: SCRUM
http://www.mountaingoatsoftware.com/topics/scrum
http://www.codeproject.com/KB/architecture/scrum.aspx
Diagram: Wikipedia

## Slide 42: V Model Overview
Requirements Analysis
Themes:
  Link front and back ends of life-cycle for efficiency
  Provide “traceability” to ensure nothing falls through the cracks
Requirements Specification
Functional
Testing
Architectural
Design
Integration
Testing
Detailed
Design
Integration
Testing
Coding
S/W Unit
Testing
Validation provided by testing
Code
Review
Review
Review
Review

## Slide 43: 1. Requirements Specification and Validation Plan
Result of Requirements Analysis
Should contain:
  Introduction with goals and objectives of system
  Description of problem to solve
  Functional description
    provides a “processing narrative” per function
    lists and justifies design constraints
    explains performance requirements
  Behavioral description shows how system reacts to internal or external events and situations
    State-based behavior
    General control flow
    General data flow
  Validation criteria
    tell us how we can decide that a system is acceptable. (Are we done yet?)
    is the foundation for a validation test plan
  Bibliography and Appendix refer to all documents related to project and provide supplementary information

## Slide 44: 2. Architectural (High-Level) Design
Architecture defines the structure of the system
  Components
  Externally visible properties of components
  Relationships among components
Architecture is a representation which lets the designer…
  Analyze the design’s effectiveness in meeting requirements
  Consider alternative architectures early
  Reduce down-stream implementation risks
Architecture matters because…
  It’s small and simple enough to fit into a single person’s brain (as opposed to comprehending the entire program’s source code)
  It gives stakeholders a way to describe and therefore discuss the system

## Slide 45: 3. Detailed Design
Describe aspects of how system behaves
  Flow charts for control or data
  State machine diagram
  Event sequences
Graphical representations very helpful
  Can provide clear, single-page visualization of what system component should do
Unified Modeling Language (UML)
  Provides many types of diagrams
  Some are useful for embedded system design to describe structure or behavior

## Slide 46: State Machine for Parsing NMEA-0183
Start
Talker + Sentence Type
Sentence Body
Checksum 1
Checksum 2
$ Append char to buf.
Any char. except *, \r or \n
Append char to buf. Inc. counter
*, \r or \n, non-text, or counter>6
buf==$SDDBT, $VWVHW, or $YXXDR
Enqueue all chars. from buf
Any char. except *
Enqueue char
*
Enqueue char
Any char.
Save as checksum1
/r or /n
Any char.
Save as checksum2

## Slide 47: Flowcharts

## Slide 48: Sequence of Interactions between Components

## Slide 49: 4. Coding and Code Inspections
Coding driven directly by Detailed Design Specification
Use a version control system while developing the code
Follow a coding standard
  Eliminate stylistic variations which make understanding code more difficult
  Avoid known questionable practices
  Spell out best practices to make them easier to follow
Perform code reviews
Test effectively
  Automation
  Regression testing

## Slide 50: Peer Code Review
Inspect the code before testing it
Extensive positive industry results from code inspections
  IBM removed 82% of bugs
  9 hours saved by finding each defect
  For AT&T quality rose by 1000% and productivity by 14%
Finds bugs which testing often misses
  80% of the errors detected by HP’s inspections were unlikely to be caught by testing
  HP, Shell Research, Bell Northern, AT&T: inspections 20-30x more efficient than testing

## Slide 51: 5. Software Testing
Testing IS NOT “the process of verifying the program works correctly”
  The program probably won’t work correctly in all possible cases
    Professional programmers have 1-3 bugs per 100 lines of code after it is “done”
  Testers shouldn’t try to prove the program works correctly (impossible)
    If you want and expect your program to work, you’ll unconsciously miss failure because human beings are inherently biased
The purpose of testing is to find problems quickly
  Does the software violate the specifications?
  Does the software violate unstated requirements?
The purpose of finding problems is to fix the ones which matter
  Fix the most important problems, as there isn’t enough time to fix all of them
  The Pareto Principle defines “the vital few, the trivial many”
    Bugs are uneven in frequency – a vital few contribute the majority of the program failures. Fix these first.

## Slide 52: Approaches to Testing
Incremental Testing
  Code a function and then test it (module/unit/element testing)
  Then test a few working functions together (integration testing)
    Continue enlarging the scope of tests as you write new functions
  Incremental testing requires extra code for the test harness
    A driver function calls the function to be tested
    A stub function might be needed to simulate a function called by the function under test, and which returns or modifies data.
    The test harness can automate the testing of individual functions to detect later bugs
Big Bang Testing
  Code up all of the functions to create the system
  Test the complete system
    Plug and pray

## Slide 53: Why Test Incrementally?
Finding out what failed is much easier
  With Big Bang, since no function has been thoroughly tested, most probably have bugs
  Now the question is “Which bug in which module causes the failure I see?”
  Errors in one module can make it difficult to test another module
    Errors in fundamental modules (e.g. kernel) can appear as bugs in other many other dependent modules
Less finger pointing = happier SW development team
  It’s clear who made the mistake, and it’s clear who needs to fix it
Better automation
  Drivers and stubs initially require time to develop, but save time for future testing

## Slide 54: Example Test Plan

## Slide 55: 6. Perform Project Retrospectives
Goals – improve your engineering processes
  Extract all useful information learned from the just-completed project – provide “virtual experience” to others
  Provide positive non-confrontational feedback
  Document problems and solutions clearly and concisely for future use
Basic rule: problems need solutions
Often small changes improve performance, but are easy to forget

## Slide 56: Example Postmortem Structure
Product
  Bugs
  Software design
  Hardware design
Process
  Code standards
  Code interfacing
  Change control
  How we did it
  Team coordination
Support
  Tools
  Team burnout
  Change orders
  Personnel availability