## Slide 1: Analog Interfacing

## Slide 2: Why It’s Needed
Embedded systems often need to measure values of physical parameters
These parameters are usually continuous (analog) and not in a digital form which computers (which operate on discrete data values) can process
Pressure
  Blood pressure monitor
  Altimeter
  Car engine controller
  Scuba dive computer
  Tsunami detector
Acceleration
  Air bag controller
  Vehicle stability
  Video game remote
Mechanical strain
Other
  Touch screen controller
  EKG, EEG
  Breathalyzer
Temperature
  Thermometer (do you have a fever?)
  Thermostat for building, fridge, freezer
  Car engine controller
  Chemical reaction monitor
  Safety (e.g. microprocessor processor thermal management)
Light (or infrared or ultraviolet) intensity
  Digital camera
  IR remote control receiver
  Tanning bed
  UV monitor
Rotary position
  Wind gauge
  Knobs

## Slide 3: Converting Between Analog and Digital Values

## Slide 4: The Big Picture – A Depth Gauge
Sensor detects air pressure and generates a proportional output voltage V_sensor
ADC generates a proportional digital integer (code) based on V_sensor and V_ref
Code can convert that integer to a something more useful
  first a float representing the voltage,
  then another float representing pressure,
  finally another float representing depth
Pressure Sensor
Analog to Digital Converter
// Your software
ADC_Code = ADC0->R[0];
V_sensor = ADC_code*V_ref/1023;
Pressure_kPa = 250 * (V_sensor/V_supply+0.04);
Depth_ft = 33 * (Pressure_kPa – Atmos_Press_kPa)/101.3;
V_sensor
ADC_Code
V_ref
V_sensor
ADC_Code
Voltages
V_ref
Ground
ADC Output Codes
111..111
000..000
000..001
111..110
111..101
111..100
Air Pressure

## Slide 5: Getting From Analog to Digital
A Comparator tells us “Is Vin > Vref?”
  Compares an analog input voltage with an analog reference voltage and determines which is larger, returning a 1-bit number
  E.g. Indicate if depth > 100 ft
  Set Vref to voltage pressure sensor returns with 100 ft depth.
An Analog to Digital converter [AD or ADC] tells us how large Vin is as a fraction of Vref.
  Reads an analog input signal (usually a voltage) and produces a corresponding multi-bit number at the output.
  E.g. calculate the depth
0
Vin
Vref
Comparator
0
1
0
1
Vin
Vref
Clock
A/D Converter

## Slide 6: Digital to Analog Conversion
May need to generate an analog voltage or current as an output signal
  E.g. audio signal, video signal brightness.
DAC: “Generate the analog voltage which is this fraction of Vref”
Digital to Analog Converter equation
  n = input code
  N = number of bits of resolution of converter
  Vref = reference voltage
  Vout = output voltage. Either
    Vout = Vref * n/(2N) or
    Vout = Vref * (n+1)/(2N)
    The offset +1 term depends on the internal tap configuration of the DAC – check the datasheet to be sure
0
1
0
1
Vout
Vref
D/A Converter

## Slide 7: Waveform Sampling and Quantization
A waveform is sampled at a constant rate – every Dt
  Each such sample represents the instantaneous amplitude at the instant of sampling
  “At 37 ms, the input is 1.91341914513451451234311… V”
  Sampling converts a continuous time signal to a discrete time signal
The sample can now be quantized (converted) into a digital value
  Quantization represents a continuous (analog) value with the closest discrete (digital) value
  “The sampled input voltage of 1.91341914513451451234311… V is best represented by the code 0x018, since it is in the range of 1.901 to 1.9980 V which corresponds to code 0x018.”
time
Digital value

## Slide 8: Forward Transfer Function Equations
General Equation
n = converted code
Vin = sampled input voltage
V+ref = upper voltage reference
V-ref = lower voltage reference
N = number of bits of resolution in ADC
(
)
2
/
1
2
ú
ú
û
ê
ê
ë
+
-
-
=
-
+
-
ref
ref
N
ref
in
V
V
V
V
n
(
)
2
/
1
2
ú
ú
û
ê
ê
ë
+
=
+
ref
N
in
V
V
n
676
2
/
1
5
2
30
.
3
10
=
ú
û
ê
ë
+
=
v
v
n
Simplification with V-ref = 0 V
û
ë
floor function: nearest integer I such that I <= X
floor(x+0.5) rounds x to the nearest integer
X = I
What code n will the ADC use to represent voltage Vin?

## Slide 9: Inverse Transfer Function
General Equation
n = converted code
Vin_min = minimum input voltage for code n
Vin_max = maximum input voltage for code n
V+ref = upper voltage reference
V-ref = lower voltage reference
N = number of bits of resolution in ADC
Simplification with V-ref = 0 V
What range of voltages Vin_min to Vin_max does code n represent?

## Slide 10: What if the Reference Voltage is not known?
Example - running off an unregulated battery (to save power)
Measure a known voltage and an unknown voltage
Many MCUs include an internal fixed voltage source which ADC can measure for this purpose
Can also solve for Vref
  “My ADC tells me that channel 27 returns a code of 0x6543, so I can calculate that VREFSH = 1.0V * 216/0x6543 = …

## Slide 11: Analog to Digital conversion concepts

## Slide 12: A/D – Flash Conversion
A multi-level voltage divider is used to set voltage levels over the complete range of conversion.
A comparator is used at each level to determine whether the voltage is lower or higher than the level.
The series of comparator outputs are encoded to a binary number in digital logic (a priority encoder)
Components used
  2N resistors
  2N-1 comparators
Note
  This particular resistor divider generates voltages which are not offset by ½ bit, so maximum error is 1 bit
  We could change this offset voltage by using resistors of values R, 2R, 2R ... 2R, 3R (starting at bottom)
1/8 V
2/8 V
3/8 V
4/8 V
5/8 V
6/8 V
7/8 V
+
-
Encoder
+
-
+
-
+
-
+
-
+
-
+
-
1V
V
in
Comparators
R
R
R
R
R
R
R
R
3
1
1
1
0
0
0
0

## Slide 13: ADC - Successive Approximation Conversion
Successively approximate input voltage by using a binary search and a DAC
SA Register holds current approximation of result
Set all DAC input bits to 0
Start with DAC’s most significant bit
Repeat
  Set next input bit for DAC to 1
  Wait for DAC and comparator to stabilize
  If the DAC output (test voltage) is smaller than the input then set the current bit to 1, else clear the current bit to 0
Voltage
Time
Start of
Conversion
Test voltage (DAC output)
T
1
T
2
T
3
T
4
T
5
T
6
000000
111111
100000
100100
Analog Input
know 1xxxxx, try 110000
100110
know xxxxxx, try 100000
know 10xxxx, try 101000
know 100xxx, try 100100
know 1001xx, try 100110
know 10011x, try 100111
know 100110. Done.

## Slide 14: A/D - Successive Approximation
Converter Schematic
Converter

## Slide 15: ADC Performance Metrics
Linearity measures how well the transition voltages lie on a straight line.
Differential linearity measure the equality of the step size.
Conversion time: between start of conversion and generation of result
Conversion rate = inverse of conversion time

## Slide 16: Sampling Problems
Nyquist criterion
  Fsample >= 2 * Fmax frequency component
  Frequency components above ½ Fsample are aliased, distort measured signal
Nyquist and the real world
  This theorem assumes we have a perfect filter with “brick wall” roll-off
  Real world filters have more gentle roll-off
  Inexpensive filters are even worse (e.g. first order filter is 20 dB/decade, aka 6 dB/octave)
  So we have to choose a sampling frequency high enough that our filter attenuates aliasing components adequately

## Slide 17: Inputs
Differential
  Use two channels, and compute difference between them
  Very good noise immunity
  Some sensors offer differential outputs (e.g. Wheatstone Bridge)
Multiplexing
  Typically share a single ADC among multiple inputs
  Need to select an input, allow time to settle before sampling
Signal Conditioning
  Amplify and filter input signal
  Protect against out-of-range inputs with clamping diodes

## Slide 18: Sample and Hold Devices
Some A/D converters require the input analog signal to be held constant during conversion, (e.g. successive approximation devices)
In other cases, peak capture or sampling at a specific point in time necessitates a sampling device.
This function is accomplished by a sample and hold device as shown to the right:
These devices are incorporated into some A/D converters

## Slide 19: STM32F4Discovery Analog Interfacing Peripherals

## Slide 20: STM32F40x LQFP100 Analog Interface Pins
100-pin QFP
Inputs
  16 12-bit ADC
Output
  2 12-bit DAC

## Slide 21: STM32F4 Discovery Analog I/O
Inputs
  16 external 12-bit ADC channels
Output
  2 12-bit DAC, one channel each

## Slide 22: GPIO Port Bit Circuitry in MCU
Configuration
  Direction
  MUX
  Modes
  Speed
Data
  Output (different ways to access it)
  Input
  Analogue
Locking

## Slide 23: Configuration of the GPIO registers
Mode 11
  GPIOA->MODER|=GPIO_MODER_MODERx;
PUPD 00
  GPIOA->PUPDR&=~(GPIO_PUPDR_PUPDRx);

## Slide 24: Digital to Analog Converter

## Slide 25: DAC Overview
Two independent channels
DAC1 connects to PA4;DAC2 connects to PA5
Output buffers, better ability to drive external loads
Different Data formats
DACoutput(12bit) = VREF×DOR÷4095
  Range from 0 to VREF+
Dual Channel mode
Support DMA

## Slide 26: Single DAC channel mode
Data Format
  8-bit right alignment DAC_DHR8Rx [7:0]
  12-bit left alignment DAC_DHR12Lx [15:4]
  12-bit right alignment DAC_DHR12Rx [11:0]
Buffered
  Data to output is stored in 16-word buffer DAC_DHRx
  DAC_DHRx will update DAC_DORx after one APB1 clock cycle
  If hardware trigger is selected (TENx bit in DAC_CR register) then then update will be delayed to three APB1 clock cycles after the trigger event.
  Depends on power supply voltage and output load, the analog output voltage will be available after a time tSETTLING (typically 3us) since the last update.
DACoutput = VREF×DOR÷4095 (12-BIT MODE)
  Range from 0 to VREF+

## Slide 27: TEN(Trigger Enable)
The timing diagram for when trigger is disabled (TEN=0)
When the trigger is enabled, can select external event to trigger the DAC
Can also be triggered by software

## Slide 28: DAC Control Register : DAC_CR
Lower 16 bits are for channel 1 and higher 16 bits are for channel 2
Fruitful functions: DMA, wave/noise generator, trigger
  EN bit: enable the DAC channel
  TEN bit: trigger enable bit, also decides how many clock cycles before DHR load into DOR
  TSEL bits: trigger selection
  BOFF bit: output buffer disable, to enhance the driving ability but the output may not reach 0 if enabled, set 1 to disable
  Wave bits: To generate noise wave or triangle wave (Only use when TEN is 1)

## Slide 29: DHR Data Holding Registers
CMSIS provides access to different format of data by defining different DHR
  Slightly different from single channel and dual channel

## Slide 30: Example: Waveform Generator
Configure corresponding GPIO
Enable the Clock (APB1)
Enable DAC
Configure DAC
  Mode
  Trigger
  Normal mode (not buffered)
Write to DAC DHR data register

## Slide 31: Analog to Digital Converter

## Slide 32: ADC Overview
Uses successive approximation for conversion
Supports multiple resolutions: 12, 10, 8 and 6 bits
4 injected channels and 16 regular channels
Supports single and continuous conversions
DUAL/Triple ADC mode
DMA
Analog watchdog
Temperature sensor

## Slide 33: ADC Overview
High sampling speed
Conversion range from 0 to 3.6 V
Different Supply requirement
Scan mode for automatic conversion
DUAL/Triple ADC mode
Channel by channel programmable sampling time
Interrupt generation on
  End of (Injected)conversion
  Analog watchdog
  Overrun

## Slide 34: ADC System Fundamentals
Output Registers
ADC
Analog Input
Clock

## Slide 35: Using the ADC
ADC initialization
  Configure GPIO (if using on board pins)
  Enable clock
  Enable ADC
  Select voltage reference
  Select trigger source
  Select input channel
  Select other parameters
Trigger conversion
Read results
Calibrate? Average?

## Slide 36: On-off Control
For power efficiency, the ADC module is usually turned off (even if it is clocked).
If ADON bit in ADC control register 2 is set, the module is powered on; otherwise it is powered off.
Good practical to shut down ADC whenever you are not using it.

## Slide 37: Clock Configuration
Analog Clock
  ADCCLK, common to all ADCs
  From APB2 (72Mhz) (Can be prescale by 1,2,4,8 or 16)
  Can be prescaled by 2, 4, 6 or 8, which means at most 36MHz
  ADC common control register(ADC_CCR) bit 17:16
Digital Interface Clock
  Used for registers read/write access
  From APB2 (72Mhz)
  Need to be enable individually for each channel (RCC_APB2ENR)

## Slide 38: ADC Conversion Time
Programmable sample time for all channels
Sample time register 1 to 2 (ADC_SMPRx)
Total conversion time = Tsampling + Tconversion

## Slide 39: Channel Selection
Two groups of channels
  Regular group
    Up to 16 conversions
    Consists of a sequence of conversions that can be done on any channel in any order
    Specify each sequence by configuring the ADC_SQRx registers
    Specify the total number of conversions by configuring the least 4 bits in the ADC_SQR1 register
  Injected group
    Up to 4 conversions
    Similar to regular group
    But the sequence is specified by the ADC_JSQR register
    Specify the total number of conversions by configuring the least 2 bits in the ADC_JSQR register
  Modifying either ADC_SQRx or ADC_JSQR will reset the current ADC process.

## Slide 40: Channel Selection
Three other channels
  ADC1_IN16 is internally connected to the temperature sensor
  ADC1_IN17 is internally connected to the reference voltage VREFINT
  ADC1_IN18 is connected to the VBAT. Can be use as regular or injected channel.
  But only available on the master ADC1 peripheral.

## Slide 41: Voltage Reference Selection
Input range from VREF- to VREF+
VREF+ Positive analog reference
VDDA equal to Vdd
VREF- Negative analog reference, =VSSA
VSSA Grounded and equal to VSS
By default, can convert input range from 0 to 3V

## Slide 42: Conversion Trigger Selection
Can be triggered by software
  Setting SWSTART bit in control register 2 (ADC_CR2) for regular group
  Setting JSWSTART bit in control register 2 (ADC_CR2) for injected group
Or by external trigger
  Select the trigger detection mode
  Specify the trigger event
  Different bits for specifying regular group and injected group

## Slide 43: Hardware Trigger Sources
ADC control register 2
Similar for Injected group

## Slide 44: Conversion Options Selection
Continuous?
  Single conversion or continuous conversion (CR2 CONT bit)
  Discontinuous mode available(CR1 DISCEN bit)
Sample time
Data alignment
  CR2 ALIGN
Scan mode: convert all the channels
  CR1 SCAN
Resolution
  CR1 RES[1:0]

## Slide 45: Conversion Completion
In single conversion mode
  Regular channel
    Store the result into the 16-bit ADC_DR register
    Set the EOC (end of conversion) flag
    Interrupt if EOCIE bit is set
  Injected channel
    Store the result into the 16-bit ADC_JDR1 register
    Set the JEOC (end of conversion injected) flag
    Interrupt if JEOCIE bit is set
Behave differently in other modes. And if there is a sequence of conversions, can be specified to set the flag at the end of the sequence or at the end of every conversion

## Slide 46: Result Registers
After the conversion, may need extra processing
  Offset subtraction from calibration
  Averaging: 1, 4, 8, 16 or 32 samples
  Formatting: Right justification, sign- or zero-extension to 16 bits
  Output comparison
Result registers for two groups
  ADC_DR for regular group
  ADC_JDRx(x=1..4) for injected group

## Slide 47: Common Control Register
Select different modes by writing to MULTI [4:0] bits
Prescale the clock by writing to ADCPRE bits
Enable the VBAT or the temperature sensor by setting VBATE or TSVREFE
Decide the delay between to sampling phases by writing to DELAY bits

## Slide 48: Using ADC Values
The ADC gives an integer representing the input voltage relative to the reference voltages
Several conversions may be needed
  For many applications you will need to compute the approximate input voltage
    Vin = …
  For some sensor-based applications you will need to compute the physical parameter value based on that voltage (e.g. pressure) – this depends on the sensor’s transfer function
  You will likely need to do additional computations based on this physical parameter (e.g. compute depth based on pressure)
Data type
  It’s likely that doing these conversions with integer math will lead to excessive loss of precision, so use floating point math
  AFTER you have the application working, you can think about accelerating the program using fixed-point math (scaled integers).
Sometimes you will want to output ASCII characters (to the LCD, for example). You will need to convert the floating point number to ASCII using sprintf, ftoa, or another method.

## Slide 49: Example: Temperature Sensor
ADC1 Channel 16
The minimum ADC sampling time for the temperature channel is 10 microseconds
Sampling cycles at least 110
T(°C) = {(Vsense-V25)/Avg_Slope}+25
  V25=Vsense value for 25°C(typical value:0.78V)
  Avg_Slope=average slope of the temperature vs. Vsense curve(typical value:1.3mv/°C)
  Vsense=DR×3/4096 (If Vref+=3v, Vref-=0v, 12-bit format)
  Statics really vary from board to board!
Use your finger to press the chip in the center of the board, the temperature will go high.

## Slide 50: Analog watchdog

## Slide 51: Analog Watchdog
Watchdog basically tries to detect exception and recover the MCU from specific situations.
Analog Watchdog is actually an ADC followed by one (or two) comparator(s).
ADC1 Channel 17
Set the status bit (or generate an interrupt) if voltage converted is below a lower threshold or is above a higher threshold.
Can select to watch all channels (either injected or regular groups or even both) or single channels.
Monitor analog input and bark e.g., if temperature goes crazy!

## Slide 52: Example: Power Failure Detection
Need warning of when power has failed
Use continuous mode and the analog watchdog interrupt
Do the last second jobs!
  Very limited amount of time before capacitor discharges
  Save critical information
  Turn off output devices
  Put system into safe mode
Can use a comparator to compare VREFINT (1.2V) against a fixed reference voltage Vref
Save data, money or even life if lucky enough

## Slide 53: Analog Watchdog
Put the Higher threshold into the 12 least significant bits into the ADC_HTR
Put the Lower threshold into the 12 least significant bits into the ADC_LTR
Enable the interrupt by setting the AWDIE bit in ADC_CR1 register

## Slide 54: Channel Selection
If monitor single channel then needs to select the channel
For monitoring the VREFINT (Channel 17), write 10001 into AWDCH
Need to enable the channel by writing setting the TSVREFE bit in CCR (which enables both temperature sensor and VREFINT)

## Slide 55: PID Control
Analog Watchdog can also be a good tool to implement PID control
Keep the power/temperature/pressure/speed/distance as close as possible to the targeted value.
Dynamically update the HTR and LTR for Analog Watchdog.
Refer to your control theory text book for more inspiration