## Slide 1: Using Direct Memory Access to Improve Performance

## Slide 2: Overview
Basic Concepts
DMA Peripherals in Cortex-M0+
DMA Applications
  Data Transfer
  Replacing ISRs

## Slide 3: Basic Concepts
Special hardware to read data from a source and write it to a destination
Various configurable options
  Number of data items to copy
  Source and destination addresses can be fixed or change (e.g. increment, decrement)
  Size of data item
  When transfer starts
Operation
  Initialization: Configure controller
  Transfer: Data is copied
  Termination: Channel indicates transfer has completed

## Slide 4: DMA Controller Features
4 independent channels
  Channel 0 has highest priority
8-, 16- or 32-bit transfers, data size can differ between source and destination
Modulo addressable
Can trigger with hardware signal or software
Can run continuously or periodically (“cycle-stealing”)
Hardware acknowledge/done signal

## Slide 5: DMA Controller

## Slide 6: Registers
DMA_SARn
  Source address register,
  Valid values 0 to 0x000f ffff
DMA_DARn
  Destination address register
  Valid values 0 to 0x000f ffff

## Slide 7: Status Register/Byte Count Register DMA_DSR_BCRn
Status flags: 1 indicates error
  CE: Configuration error
  BES: Bus error on source
  BED: Bus error on destination
  REQ: A transfer request is pending (more transfers to perform)
  BSY: DMA channel is busy
  DONE: Channel transfers have completed or an error occurred. Clear this bit in an ISR.

## Slide 8: Byte Count Register
BCR: Bytes remaining to transfer
Decremented by 1, 2 or 4 after completing write (determined by destination data size)

## Slide 9: DMA Control Register (DMA_DCRn)
EINT: Enable interrupt on transfer completion
ERQ: Enable peripheral request to start transfer
CS: Cycle steal
  0: Greedy - DMA makes continuous transfers until BCR == 0
  1: DMA shares bus, performs only one transfer per request
AA: Autoalign

## Slide 10: DMA Control Register (DMA_DCRn)
EADRQ – Enable asynchronous DMA requests when MCU is in Stop mode
SINC/DINC – Increment SAR/DAR by 1,2 or 4 based on size of data
SSIZE/DSIZE – Source/Destination data size.
  Don’t need to match – controller will perform extra reads or writes as needed (e.g. read one word, write two bytes).
  00: longword (32 bits)
  01: byte (8 bits)
  10: word (16 bits)
START – Write 1 to start transfer

## Slide 11: DMA Control Register (DMA_DCRn)
SMOD, DMOD – Source/Destination address modulo
  When non-zero, supports circular data buffer – address wraps around after 2n+3 bytes (16 bytes to 64 kilobytes)
  When zero, circular buffer is disabled
D_REQ: If 1, then when BCR reaches zero ERQ bit will be cleared
LINKCC: Enables this channel to trigger another channel
  00: Disabled
  01: Two stages:
    Link to channel LCH1 after each cycle-steal transfer
    Link to channel LCH2 after BCR reaches 0
  10: Link to channel LCH1 after each cycle-steal transfer
  11: Link to channel LCH1 after BCR reaches 0
LCH1, LCH2: Values 00 to 11 specify linked DMA channel (0 to 3)

## Slide 12: Basic Use of DMA
Enable clock to DMA module (in SIM register SCGC7)
Initialize control registers
Load SARn with source address
Load DARn with destination address
Load BCRn with number of bytes to transfer
Clear DSRn[DONE]
Start transfer by setting DCRn[START]
Wait for end of transfer
  Interrupt generated if DCRn[EINT] is set (DMAn_IRQHandler)
  Poll DSRn[DONE]

## Slide 13: Demonstration: Memory Copy
Software-triggered
void Copy_Longwords(uint32_t * source, uint32_t * dest, uint32_t count)
Could use as a fast version of memcpy function, but need to handle all cases
  Alignment of source and destination
  Data size
  Detecting overlapping buffers

## Slide 14: Triggering DMA Activity Using Peripherals
Can use trigger events from peripherals to start DMA transfer
Upon triggering, DMA can perform:
  One transfer (cycle steal mode)
  All transfers until BCR == 0 (continuous mode)
DMA Multiplexer (DMAMUX)
  Selects which source will trigger a DMA channel
Each DMA channel n has a configuration register DMAMUX_CHCFGn
  ENBL: Enable DMA channel
  TRIG: Enables triggering of DMA channel
  SOURCE: Selects triggering source

## Slide 15: Trigger Sources
Trigger sources are chip-specific, so see KL25 Sub-Family Reference Manual (rev. 1), Chapter 3 - Chip Configuration, Section 3.4.8.1 DMA MUX Request Sources
Source # | Module | Description
0 | - | Disabled
2-7 | UART0,1, 2 | Receive, Transmit
16-19 | SPI0, 1 | Receive, Transmit
22-23 | I2C0, 1 | 
24-29 | TPM0 | Channels 0-5
32-35 | TPM1-2 | Channels 0-1
40 | ADC0 | 
42 | CMP0 | 
45 | DAC0 | 
49-53 | Port Control Module | Port A-E
54-56 | TPM0-2 | Overflow
57 | TSI | 
60-63 | DMAMUX | Always enabled

## Slide 16: Triggering DMA Transfers with PITs
DMA Channels 0, 1 can be triggered by PITs 0 and 1 as well as the previously listed sources
PIT generates a trigger pulse each time it reaches 0
  Disable interrupt for PITn by clearing TIE (interrupt enable) bit.
  Clear ENBL and TRIG bits in CHCFGn register
  Configure DMA Controller channel
  Configure timer
  Select trigger source with CHCFGn register and set ENBL and TRIG bits

## Slide 17: Demonstration of ISR Replacement: DAC Playback
TPM0 expires each time we need to update the DAC
When DMA is triggered by TPM:
  Copy one 16-bit data element from wave table (source) to DAC data register (DAC0->DAT[0])
  Increment source address, decrement byte count
When DMA finishes last transfer
  Generate interrupt
  IRQ handler will clear interrupt flags, restart DMA transfers
DMA Configuration
  Source, destination sizes = 2 bytes: SSIZE = DSIZE = 2
  Enable peripheral request: ERQ = 1
  Select hardware trigger
  One transfer per peripheral request, so use cycle-steal mode: CS = 1
  Two bytes per transfer: BCR = 2 bytes
  Increment source register: SINC = 1
  Do not increment destination register: DINC = 0
TPM Configuration
  Don’t enable timer interrupt
  TPM will still generate trigger event

## Slide 18: Performance Comparison
Traces
  Yellow: ISR is executing when trace is low
  Blue: DAC output (PTE30, pin 11 of J10)
Without DMA: Interrupt per sample
  4.7 microseconds per 620 microseconds
  0.758% of processor’s time
With DMA: Interrupt per cycle
  5.0 microseconds per 20 milliseconds
  0.025% of processor’s time
How is this useful?
  Saves CPU time
  Reduces timing vulnerability to interrupts being disabled
  Enables CPU to sleep longer, wake up less often (20 milliseconds vs. 620 microseconds)