## Slide 1: Timer Peripherals

## Slide 2: KL25 Timer Peripherals
PIT - Periodic Interrupt Timer
  Can generate periodically generate interrupts or trigger DMA (direct memory access) transfers
TPM - Timer/PWM Module
  Connected to I/O pins, has input capture and output compare support
  Can generate PWM signals
  Can generate interrupts and DMA requests
LPTMR - Low-Power Timer
  Can operate as timer or counter in all power modes (including low-leakage modes)
  Can wake up system with interrupt
  Can trigger hardware
Real-Time Clock
  Powered by external 32.768 kHz crystal
  Tracks elapsed time (seconds) in 32-bit register
  Can set alarm
  Can generate 1Hz output signal and/or interrupt
  Can wake up system with interrupt
SYSTICK
  Part of CPU core’s peripherals
  Can generate periodic interrupt

## Slide 3: Timer/Counter Peripheral Introduction
Common peripheral for microcontrollers
Based on presettable binary counter, enhanced with configurability
  Count value can be read and written by MCU
  Count direction can often be set to up or down
  Counter’s clock source can be selected
    Counter mode: count pulses which indicate events (e.g. odometer pulses)
    Timer mode: clock source is periodic, so counter value is proportional to elapsed time (e.g. stopwatch)
  Counter’s overflow/underflow action can be selected
    Generate interrupt
    Reload counter with special value and continue counting
    Toggle hardware output signal
    Stop!
Events
Clock
Current Count
Reload Value
Presettable Binary Counter
÷2 or RS
PWM
Interrupt
Reload
or

## Slide 4: Periodic Interrupt Timer

## Slide 5: PIT - Periodic Interrupt Timer
Generates periodic interrupts with specified period

## Slide 6: Periodic Interrupt Timer
32-bit counter
Load start value (32-bit) from LDVAL
Counter counts down with each clock pulse
  Fixed clock source for PIT - Bus Clock from Multipurpose Clock Generator - e.g. 24 MHz
When timer value (CVAL) reaches zero
  Generates interrupt
  Reloads timer with start value
Clock
Read current timer value (TVL) from PIT_CVALn
Presettable Binary Counter
Interrupt
Reload
Start Value
Read/write timer start value (TSV) from PIT_LDVALn
Write 1000 to TSV
Enabling timer loads counter with 1000, starts counting
TVL counts down to 0
PIT interrupt generated, counter reloads with 1000, starts counting
Write 700 to TSV
PIT interrupt generated, counter reloads with 400, starts counting
PIT interrupt generated, counter reloads with 400, starts counting
PIT interrupt generated, counter reloads with 400, starts counting
PIT Interrupt

## Slide 7: PIT Configuration
First: Clock gating
  SIMCGC6 PIT
Second: Module Control Register (PIT->MCR)
  MDIS - Module disable
    0: module enabled
    1: module disabled (clock disabled)
  FRZ - Freeze - stops timers in debug mode
    0: timers run in debug mode
    1: timers are frozen (don’t run) in debug mode
Multiple timer channels within PIT
  KL25Z has two channels
Can chain timers together to create 64-bit timer

## Slide 8: Control of Each Timer Channel n
CMSIS Interface:
  General PIT settings accessed as struct: PIT->MCR, etc.
  Channels are accessed as an array of structs: PIT->CHANNEL[n].LDVAL, etc
PIT_LDVALn: Load value (PIT->CHANNEL[n].LDVAL)
PIT_CVALn: Current value (PIT->CHANNEL[n].CVAL)
PIT_TCTRLn: Timer control (PIT->CHANNEL[n].TCTRL)
  CHN: Chain
    0: independent timer operation, uses own clock source
    1: timer n is clocked by underflow of timer n-1
  TIE: Timer interrupt enable
    0: Timer will not generate interrupts
    1: Interrupt will be requested on underflow (i.e. when TIF is set)
  TEN: Timer enable
    0: Timer will not count
    1: Timer is enabled, will count
PIT_TFLG0: Timer flags
  TIF: Timer interrupt flag
    1: Timeout has occurred

## Slide 9: Configuring the PIT
Enable clock to PIT module
  SIM->SCGC6 |= SIM_SCGC6_PIT_MASK;
Enable module, freeze timers in debug mode
  PIT->MCR &= ~PIT_MCR_MDIS_MASK;
  PIT->MCR |= PIT_MCR_FRZ_MASK;
Initialize PIT0 to count down from starting_value
  PIT->CHANNEL[0].LDVAL = PIT_LDVAL_TSV(starting_value);
No chaining of timers
  PIT->CHANNEL[0].TCTRL &= PIT_TCTRL_CHN_MASK;

## Slide 10: Calculating Load Value
Goal: generate an interrupt every T seconds
LDV = round(T*fcount - 1)
  -1 since the counter counts to 0
  Round since LDV register is an integer, not a real number
    Rounding provides closest integer to desired value, resulting in minimum timing error
Example: Interrupt every 137.41 ms
  LDV = 137.41 ms * 24 MHz - 1 = 3297839
Example: Interrupt with a frequency of 91 Hz
  LDV = (1/91 Hz)*24 MHz - 1 = round (263735.2637-1) = 263734

## Slide 11: Configuring the PIT and NVIC for Interrupts
Configure PIT
  Let the PIT channel generate interrupt requests
    PIT->CHANNEL[0].TCTRL |= PIT_TCTRL_TIE_MASK;
Configure NVIC
  Set PIT IRQ priority
    NVIC_SetPriority(PIT_IRQn, 128); // 0, 64, 128 or 192
  Clear any pending IRQ from PIT
    NVIC_ClearPendingIRQ(PIT_IRQn);
  Enable the PIT interrupt in the NVIC
    NVIC_EnableIRQ(PIT_IRQn);
Make sure interrupts are not masked globally
    __enable_irq();

## Slide 12: Interrupt Handler
One interrupt for entire PIT
CMSIS ISR name: PIT_IRQHandler
ISR activities
  Clear pending IRQ
    NVIC_ClearPendingIRQ(PIT_IRQn);
  Determine which channel triggered interrupt
    if (PIT->CHANNEL[n].TFLG & PIT_TFLG_TIF_MASK) {
  Clear interrupt request flag for channel
    PIT->CHANNEL[0].TFLG &= PIT_TFLG_TIF_MASK;
  Do the ISR’s work

## Slide 13: Starting and Stopping the Timer Channel
Start the timer channel
  PIT->CHANNEL[0].TCTRL |= PIT_TCTRL_TEN_MASK;
Stop the timer channel
  PIT->CHANNEL[0].TCTRL &= ~PIT_TCTRL_TEN_MASK;

## Slide 14: Example: Stopwatch
Measure time with 100 us resolution
Display elapsed time, updating screen every 10 ms
Controls
  S1: toggle start/stop
Use PIT
  Counter increment every 100 us
    Set to PIT Channel 0 to expire every 100 us
    Calculate load value LDVAL = round (100 us * 24 MHz -1) = 2399
  LCD Update every 10 ms
    Update LCD every nth PIT ISR
    n = 10 ms/100us = 100
    Don’t update LCD in ISR! Too slow.
    Instead set flag LCD_Update in ISR, poll it in main loop

## Slide 15: Timer/PWM Module (TPM)

## Slide 16: TPM - Timer/PWM Module
Core: Module counter
  Two clock options - external or internal
  Prescaler to divide clock by 1 to 128
  16-bit counter
    Can count up or up/down
    Can reload with set load value or wrap around (to FFFF or 0000)
Six channels
  3 modes
    Capture Mode: capture timer’s value when input signal changes
    Output Compare: Change output signal when timer reaches certain value
    PWM: Generate pulse-width-modulated signal. Width of pulse is proportional to specified value.
  Each channel can generate interrupt, DMA request, hardware trigger on overflow
  One I/O pin per channel TPM_CHn

## Slide 17: Timer Configuration
Clock source
  CMOD: selects internal or external clock
Prescaler
  PS: divide selected clock by 1, 2, 4, 8, 16, 32,64, 128
Count Mode and Modulo
  CPWMS: count up (0) or up and down (1)
  MOD: 16-bit value up to which the counter counts
    Up counting: 0, 1, 2, … MOD, 0/Overflow, 1, 2, … MOD
    Up/down counting: 0, 1, 2, … MOD, MOD-1/Interrupt, MOD-2, … 2, 1, 0, 1, 2, …
Timer overflows when counter goes 1 beyond MOD value
DMA: Enable DMA transfer on overflow
TOF: Flag indicating timer has overflowed

## Slide 18: Basic Counter Mode
Count external events applied on input pin
  Set CMOD = 01 to select external clock
  Set PS = 000 (unless division needed
Timer overflow flag TOF set to 1 upon receiving MOD * prescaler pulses
Can generate interrupt if TOIE is set
2-0 PS | Prescaler Factor
000 | 1
001 | 2
010 | 4
011 | 8
100 | 16
101 | 32
110 | 64
111 | 128

## Slide 19: Count Mode and Modulo - Counting Up

## Slide 20: Count Mode and Modulo - Counting Up and Down

## Slide 21: TPM Configuration (TPMx_CONF)
TRGSEL - input trigger select
CROT - counter reload on trigger
CSOO - counter stop on overflow
CSOT - counter start on trigger
GTBEEN - external global time base enable (rather than LPTPM counter)
DBGMODE - let LPTPM counter increment during debug mode
DOZEEN - pause LPTPM when in doze mode

## Slide 22: TPM Status (TPMx_STATUS)
TOF - LPTPM counter has overflowed
CHxF - Channel event has occurred (event depends on mode)

## Slide 23: Major Channel Modes
Input Capture Mode
  Capture timer’s value when input signal changes
    Rising edge, falling edge, both
  How long after I started the timer did the input change?
    Measure time delay
Output Compare Mode
  Modify output signal when timer reaches specified value
    Set, clear, pulse, toggle (invert)
  Make a pulse of specified width
  Make a pulse after specified delay
Pulse Width Modulation
  Make a series of pulses of specified width and frequency

## Slide 24: Channel Configuration and Value
Configuration: TPMx_CnSC
  CHF - set when event occurs
  CHIE - enable channel to generate an interrupt
  MSB:MSA - mode select
  ELSB:ELSA - edge or level select
  DMA - enable DMA transfers
Value: TPMx_CnV
  16-bit value for output compare or input capture

## Slide 25: Input Capture Mode
Select mode with CPWMS = 0, MSnB:MSnA = 00
TPM_CHn I/O pin operates as edge- sensitive input
  ELSnB:ELSnA select rising (01) or falling edge (10) or both (11)
When valid edge is detected on TPM_CHn…
  Current value of counter is stored in CnV
  Interrupt is enabled (if CHnIE = 1)
  CHnF flag is set (after 3 clock delay)
TPM_CHn
CnV
initialized value
3

## Slide 26: Wind Speed Indicator (Anemometer)
Rotational speed (and pulse frequency) is proportional to wind velocity
Two measurement options:
  Frequency (best for high speeds)
  Width (best for low speeds)
Can solve for wind velocity v
How can we use the TPM for this?
  Use Input Capture Mode to measure period of input signal

## Slide 27: TPM Capture Mode for Anemometer
Configuration
  Set up TPM to count at given speed from internal clock
  Set up TPM channel for input capture on rising edge
Operation: Repeat
  First TPM interrupt - on rising edge
    Reconfigure channel for input capture on falling edge
    Clear TPM counter, start it counting
  Second TPM interrupt - on falling edge
    Read capture value from CnV, save for later use in wind speed calculation
    Reconfigure channel for input capture on rising edge
    Clear TPM counter, start it counting

## Slide 28: Output Compare Mode
Select mode with CPWMS = 0, MSnA = 1
TPM_CHn I/O pin operates as output, MSnB and ELSnB:ELSnA select action on match
  If MSnB = 0
    Toggle (01)
    Clear (00)
    Set (11)
  If MSnB = 1
    Pulse low (10)
    Pulse high (x1)
When CNT matches CnV …
  Output signal is generated
  CHnF flag is set
  CHnI Interrupt is enabled (if CHnIE = 1)

## Slide 29: Pulse-Width Modulation
Uses of PWM
  Digital power amplifiers are more efficient and less expensive than analog power amplifiers
    Applications: motor speed control, light dimmer, switch-mode power conversion
    Load (motor, light, etc.) responds slowly, averages PWM signal
  Digital communication is less sensitive to noise than analog methods
    PWM provides a digital encoding of an analog value
    Much less vulnerable to noise
PWM signal characteristics
  Modulation frequency – how many pulses occur per second (fixed)
  Period – 1/(modulation frequency)
  On-time – amount of time that each pulse is on (asserted)
  Duty-cycle – on-time/period
  Adjust on-time (hence duty cycle) to represent the analog value

## Slide 30: TPM Channel for PWM Mode
Edge-aligned - leading edges of signals from all PWM channels are aligned
  Uses count up mode
  Period = (MOD + 1) cycles
  Pulse width = (CnV) cycles
MSnB:MSnA = 01, CPWMS = 0
  ELSnB:ELSnA = 10 - high-true pulses
  ELSnB:ELSnA = x1 - low-true pulses

## Slide 31: TPM Channel for PWM Mode
Center-aligned - centers of signals from all PWM channels are aligned
  Uses count up/down mode
  Period = 2*MOD cycles. 0x0001 <= MOD <= 0x7FFFF
  Pulse width = 2*CnV cycles
MSnB:MSnA = 10, CPWMS = 1
  ELSnB:ELSnA = 10 - high-true pulses
  ELSnB:ELSnA = x1 - low-true pulses

## Slide 32: PWM to Drive Servo Motor
Servo PWM signal
  20 ms period
  1 to 2 ms pulse width

## Slide 33: Low Power Timer (LPTMR)

## Slide 34: LPTMR Overview
Features
  16 bit counter
  Can count time or external pulses
  Can generate interrupt when counter matches compare value
  Interrupt wakes MCU from any low power mode
Registers
  Control Status register LPTMRx_CSR
  Prescale register LPTMRx_PSR
  Counter register LPTMRx_CNR
  Compare register LPTRMx_CMR

## Slide 35: Control Status Register
TCF: Timer Compare Flag
  1 if CNR matches CMR and increments
TIE: Timer Interrupt Enable
  Set to 1 to enable interrupt when TCF == 1
TPS: Timer Pin Select for pulse counter mode
  Inputs available depend on chip configuration, see KL25 SRM Chapter 3: Chip Configuration

## Slide 36: Control Status Register
TPP: Timer Pin Polarity
  0: input is active high, increments CNR on rising edge
  1: input is active low, increments CNR on falling edge
TFC: Timer Free-running Counter
  0: Reset CNR whenever TCF is set (on match)
  1: Reset CNR on overflow (wrap around)
TMS: Timer Mode Select
  0: Time counter
  1: Pulse counter
TEN: Timer Enable
  1: Enable LPTMR operation

## Slide 37: Prescale Register
PRESCALE: divide by 2 to 65536
  Time counter mode: Divide input clock by 2PRESCALE+1
  Pulse counter mode: Is glitch filter which recognizes input signal change after 2PRESCALE rising clock cycles
PBYP: Prescaler Bypass
  0: use prescaler
  1: bypass prescaler
PCS: Prescaler Count Select
  Inputs available depend on chip configuration, see KL25 SRM Chapter 3: Chip Configuration